## Slide 1: Introduction to Intelligent Vehicles [ 7. Intersection Management ]
Chung-Wei Lin
cwlin@csie.ntu.edu.tw
CSIE Department
National Taiwan University
Fall 2019

## Slide 2: Announcement
Homework
  Homework 2
    Graded?
    Reminder: if you answer M = 2018…
    Reminder: signal packing
    Regrade request due on October 30 (Wednesday) 11:59pm
  Homework 3
    Will be posted before or on November 4 (Monday)
    Due on November 25 (Monday) noon
Project
  Proposal
    Due on November 18 (Monday) noon

## Slide 3: Where Are We Now?
Four parts in sequence
  [Part 1] Preliminary
  [Part 2] Applications
  [Part 3] Intelligent Technology
  [Part 4] Advanced Topics
functional model
τ3
σ1
μ1,1
μ1,2
τ2
τ1
τ6
τ5
τ4
τ8
τ7
σ2
σ3
σ4
σ5
σ6
ε2
ε1
μ2,1
μ2,2
ε3
architecture platform

## Slide 4: Intersection Management
What is intersection management?
  Decide who goes first
Why is intersection management helpful?
  Make the intersection safer and traffic smoother and more efficient
When is intersection management working?
  Anytime?
Where is intersection management working?
  Centralized vs. distributed
Who develops intersection management?
  Basic ones from governments (or their suppliers)
  Advanced ones have not been realized
How does intersection management work?

## Slide 5: Ideal Intersection

## Slide 6: Outline
Modeling
  Note: not all following models will be used at the same time
Controlling Lengths of Traffic Lights
Intelligent Intersection Management
Imperfect Communication
Centralized and Distributed Approaches
Graph-Based Approach
Non-Cooperative Environment

## Slide 7: Tiles (Cells)
Usually, higher granularity, e.g., smaller tiles, more detailed management and higher complexity
  Example: an intersection with 20 tiles
  Example: an intersection with 64 tiles
  Example: a roundabout with 24 tiles
Chen and Englund, "Cooperative intersection management: A survey," IEEE Transactions on Intelligent Transportation Systems, 2016.

## Slide 8: Trajectories
The trajectories for vehicles from different directions with different intentions follows "pre-defined" routes
  Example: 1 trajectory for each direction of the intersection
  Example: 3 trajectories for each direction of the intersection
  Example: 4 trajectories for each direction of the roundabout
Chen and Englund, "Cooperative intersection management: A survey," IEEE Transactions on Intelligent Transportation Systems, 2016.

## Slide 9: Collision Zones (Conflict Regions)
Intersections of trajectories
The fundamental goal
  We should not let two vehicles occupy a collision zone or a tile at the same time
Chen and Englund, "Cooperative intersection management: A survey," IEEE Transactions on Intelligent Transportation Systems, 2016.

## Slide 10: Phases
Example
  8 phases of an intersection

## Slide 11: Outline
Modeling
Controlling Lengths of Traffic Lights
Intelligent Intersection Management
Imperfect Communication
Centralized and Distributed Approaches
Graph-Based Approach
Non-Cooperative Environment

## Slide 12: Controlling Lengths of Traffic Lights
Fixed time control
Coordinated control
  Continuous green lights
Adaptive control
  Design-time approach
    Based on traffic data and history
  Real-time approach
    Based on sensor observation or communication

## Slide 13: Back-Pressure Control: Method
Traffic flow is similar to water flow
Basic notation
  λi: lane i
  Qi: queue length of lane i
  Pi: pressure of lane i
    Pi = Qi
  Di,j: [0,1] there is a vehicle waiting at lane i to leave from lane i for lane j
  Pi,j: pressure from lane i to lane j
    Pi,j = Di,j max(Pi – Pj, 0)
Each time slot, pick a phase which can maximize ∑(i,j) Vi,j Pi,j
  Vi,j: the maximum number of vehicles that can go from lane i to lane j in the phase during the time slot

## Slide 14: Back-Pressure Control: Example
Computation
  λ1, λ2, λ3, λ4, λ5, λ6
  Q = {0, 2, 0, 1, 0, 1}
  P = {0, 2, 0, 1, 0, 1}
  D2,1 = D2,5 = D4,1 = D6,5 = 1
  P2,1 = P2,5 = 2 and P4,1 = P6,5 = 1
  Assume Vi,j is V or 0
    Why 0?
  (Check animations for phases)
  ∑(i,j) Vi,j Pi,j = 4V for Phase 1
  ∑(i,j) Vi,j Pi,j = 2V for Phase 2
  ∑(i,j) Vi,j Pi,j = 3V for Phase 3
  Pick Phase 1
To 5
To 1
To 5
1
To 1
2
3
4
5
6
1
2
3
4
5
6

## Slide 15: Back-Pressure Control: Extensions
Capacity-aware back-pressure control
  Remove the assumption of infinite capacity
  Improve the fairness (for low density traffic)
  Redefine Pi as another more complicated function
Adaptive max-pressure control
  Model the network demand with a constant average rate
  Provide some stability and performance guarantees
  Redefine Pi as another more complicated function

## Slide 16: Controlling Lengths of Traffic Lights
If the lengths of green, yellow, and red lights can be very short

## Slide 17: Outline
Modeling
Controlling Lengths of Traffic Lights
Intelligent Intersection Management
Imperfect Communication
Centralized and Distributed Approaches
Graph-Based Approach
Non-Cooperative Environment

## Slide 18: Assumptions
All vehicles are connected and autonomous
  If not connected
    Need road-side units to collect traffic information, e.g., vehicles coming
    Need traffic lights to provide instructions
  If not autonomous
    Need to consider the control capability of human drivers

## Slide 19: Goals
Safety
Traffic efficiency
Deadlock and starvation avoidance
Low communication and computation complexity
Incremental deployability
Protocol standardization
Dresner and Stone, "A multiagent approach to autonomous intersection management," Journal of Artificial Intelligence Research, 2008.

## Slide 20: Intelligent Intersection Management
Vehicle
  Send a request to the intersection manager about its intention
  Do not enter the intersection before confirmation
Intersection manager
  Resolve conflicts through scheduling policies
  Allocate tiles (cells) to vehicles for every time step
  Send confirmations or rejections to vehicles
Dresner and Stone, "A multiagent approach to autonomous intersection management," Journal of Artificial Intelligence Research, 2008.

## Slide 21: Vehicle Behavior
Message types
  REQUEST to make a reservation
  CHANGE-REQUEST to change a reservation
    REQUEST and CHANGE-REQUEST include all the relevant properties of the vehicle
  CANCEL to cancel an existing reservation
  DONE after crossing the intersection
    CANCEL and DONE include the IDs of the vehicle and the reservation
Not enter the intersection if there is no confirmation from the manager
Dresner and Stone, "A multiagent approach to autonomous intersection management," Journal of Artificial Intelligence Research, 2008.

## Slide 22: Manager Behavior
Message types
  CONFIRM after approving a REQUEST or CHANGE-REQUEST
    ID of the reservation
    Start time
    Start and departure lanes
    A list of constraints for the vehicle's acceleration in the intersection
  REJECT to reject a REQUEST or CHANGE-REQUEST
  ACKNOWLEDGE to respond a CANCEL or DONE
  EMERGENCY-STOP when detecting a major problem
Control policies
  First come (definition?), first served
  "Virtual" stop sign
  "Virtual" traffic light
Dresner and Stone, "A multiagent approach to autonomous intersection management," Journal of Artificial Intelligence Research, 2008.

## Slide 23: Outline
Modeling
Controlling Lengths of Traffic Lights
Intelligent Intersection Management
Imperfect Communication
Centralized and Distributed Approaches
Graph-Based Approach
Non-Cooperative Environment

## Slide 24: Modeling Vehicle Behavior
[4s,5s]: example time of feasible "entering" the intersection
  This is a logical view --- the number can be estimated by the manager
Reasons of slowing down
  Sense the intersection in front and not receive a confirmation
  Sense other vehicles in front
Not Requested Yet
Requested (Changed)
Confirmed
Approaching / REQUEST [4,5]
CONFIRM [5,6] /
Changing status 1 / CHANGE-REQUEST [5,6]
CONFIRM [5,6] /
Not doable /
Requested
Doable /
Entered
Changing status 1 / CHANGE-REQUEST [6,7]
Left
Leaving intersection / DONE
Changing status 2 / CANCEL or REJECT /
Changing status 2 / CANCEL or REJECT /

## Slide 25: Imperfect Communication: Loss
Informal analysis
  Case 1/2: What if a REQUEST/CHANGE-REQUEST is lost?
  Case 3: What if a CANCEL is lost?
  Case 4: What if a DONE is lost?
  Case 5: What if a CONFIRM is lost?
  Case 6: What if a REJECT is lost?
  Case 7: What if an ACKNOWLEDGE is lost?
  Case 8: What if an EMERGENCY-STOP is lost?
Ideally, we should have "formal analysis"
Having "timeouts" is important
  Re-request a reservation (Cases 1, 2, 5, 6)
  Logically remove a vehicle after physically checking the intersection? (Case 4)

## Slide 26: Imperfect Communication: Delay
Informal analysis
  Case 1/2: What if a REQUEST/CHANGE-REQUEST is delayed?
  Case 3: What if a CANCEL is delayed?
  Case 4: What if a DONE is delayed?
  Case 5: What if a CONFIRM is delayed?
  Case 6: What if a REJECT is delayed?
  Case 7: What if an ACKNOWLEDGE is delayed?
  Case 8: What if an EMERGENCY-STOP is delayed?
Combinations of message loss and delay
  How do you know which vehicle is in front?
Having "time stamps" can help
  Synchronization protocol?

## Slide 27: Imperfect Communication: More
Schedule only when 1st vehicle requests (otherwise?)
  We assume that each vehicle knows if it is 1st vehicle and provides this information to the manager
X |  | Missing X-Request | Missing X-Confirmation
1st Vehicle | Manager | Schedule nothing (1st vehicle missing) | Schedule all vehicles
 | 1st Vehicle | Slow down, timeout, re-request | Slow down, timeout, re-request
 | 2nd Vehicle | Slow down, timeout, re-request | Slow down, cannot make it, re-request
 | 3rd Vehicle | Slow down, timeout, re-request | Slow down, cannot make it, re-request
2nd Vehicle | Manager | Schedule 1st and 3rd vehicles | Schedule all vehicles
 | 1st Vehicle | Normal | Normal
 | 2nd Vehicle | Slow down, timeout, re-request | Slow down, timeout, re-request
 | 3rd Vehicle | Slow down, cannot make it, re-request | Slow down, cannot make it, re-request
3rd Vehicle | Manager | Schedule 1st and 2nd vehicles | Schedule all vehicles
 | 1st Vehicle | Normal | Normal
 | 2nd Vehicle | Normal | Normal
 | 3rd Vehicle | Slow down, timeout, re-request | Slow down, timeout, re-request

## Slide 28: Outline
Modeling
Controlling Lengths of Traffic Lights
Intelligent Intersection Management
Imperfect Communication
Centralized and Distributed Approaches
Graph-Based Approach
Non-Cooperative Environment

## Slide 29: System Block Diagram: Centralized
The manager is the decision maker
Vehicle i
Motion Planning
Controller
Receiver
Sender
Vehicle 1
Vehicle 2
Manager (Decision Making)
Vehicle 3
Vehicle 4
Constraints from Manager
Trajectory
Time to Occupy
Conflict Zones

## Slide 30: Flow of Execution: Centralized
Each task should be completed in time
Decision Making
Communication
Motion Planning
Controller
Time

## Slide 31: System Block Diagram: Distributed
Each vehicle is a decision maker
Vehicle i
Motion Planning
Controller
Receiver
Sender
Vehicle 1
Vehicle 2
Vehicle 3
Vehicle 4
Constraints
Trajectory
Time to Occupy
Conflict Zones
Decision Making
Other Vehicles'
Information

## Slide 32: Flow of Execution: Distributed
Each task should be completed in time
Communication
Decision Making
Motion Planning
Controller
Time

## Slide 33: Outline
Modeling
Controlling Lengths of Traffic Lights
Intelligent Intersection Management
Imperfect Communication
Centralized and Distributed Approaches
Graph-Based Approach
Non-Cooperative Environment

## Slide 34: Graph-Based Policy
The decision making problem in intersection management can be transformed to a cycle-removal problem in a graph
Generalization
  Conflict-resolution problem
    The goal: we should not let two vehicles occupy a conflict zone (or a tile) at the same time
  Distributed intersection management
    Does it make sense to have no manager?
    If vehicles (even from different OEMs) agree how to remove a cycle, then "conflict-free" can be guaranteed
    Cycle-removal algorithm is the "agreement" between vehicles (e.g., four-way stop sign) in a distributed setting
      We have an existing system in …

## Slide 35: Intersection
Intersection
  There is one intersection
Intersection manager
  Receive the information from vehicles
  Assign a time window to each vehicle at each location (conflict zone) on the trajectory of the vehicle
(( ))
(( ))
Roadside Unit
(( ))
(( ))
(( ))

## Slide 36: Vehicle
Vehicle
  All vehicles are connected and autonomous
  Each vehicle has a fixed trajectory
  Vehicle does not change lanes before and after the intersection
(( ))
(( ))
Roadside Unit
(( ))
(( ))
(( ))

## Slide 37: Conflict Zone
Conflict zone
  A conflict zone is the crossing location of two trajectories
  Two vehicles cannot be at (occupy) the same conflict zone at the same time
Conflict Zone

## Slide 38: Timing Conflict Graph
Timing conflict graph
  A directed timing conflict graph G = (V, E) is constructed
  Vertex set vi,j is a subset of the Cartesian product of the sets of vehicles and conflict zones
  Edge
    Type-1: same vehicle's trajectoty
    Type-2: conflicts between different vehicles from the same lane
    Type-3: conflicts between different vehicles from different lanes
4
1
2
3
4
1
2
3
1,1
1,2
1,3
2,1
3,3
3,4
4,4
4,1
Type-1
Type-2
Type-3

## Slide 39: Model Expressiveness
If the intersection is modeled by only one conflict zone
  Its expressiveness is limited, and the two vehicles cannot enter the intersection at the same time
If the intersection is modeled by four conflict zones
  Two vehicles can enter the intersection at the same time
1
1,1
2,1
1
2
4
1
2
3
1,1
1,2
1,3
2,1
2,3
2,4
1
2
Type-1
Type-2
Type-3

## Slide 40: Goals
A cycle-removal algortihm to
  Minimize
    The passing time of the last vehicle, or
    The average delay of vehicles
  Guarantee collision-freeness
    Provided by the passing order and scheduling after removing cycles
  Guarantee deadlock-freeness
    Graph-based verification
    Petri-Net-based verification
4
1
2
3
4
1
2
3
1,1
1,2
1,3
2,1
3,3
3,4
4,4
4,1
Type-1
Type-2
Type-3

## Slide 41: Graph-Based Verification
Having no cycles in G does not guarantee deadlock-freeness
  There are deadlocks in (a), (b), (c)
  There are no deadlocks in (d), (e)
Type-1
Type-2
Type-3
1,1
1,2
2,1
2,2
1,1
1,2
2,1
2,2
1,1
2,2
2,1
2,3
1,3
1,1
2,2
2,1
2,3
1,3
(a)
(d)
(b)
(e)
1,1
2,1
1,3
2,2
3,2
3,3
(c)

## Slide 42: Graph-Based Verification
Construction of resource conflict graph
  The directed resource conflict graph is constructed by following rules
i, j
vi, j in G'
i, j, j'
ui, j, j' in H'
i, j'
i, j
i, j''
i, j, j'
i, j', j''
(a)
i, j
i, j'
i', j
i', j''
i, j, j'
i', j, j''
i, j
i, j'
i', j''
i', j
i, j, j'
i', j'', j
i, j'
i, j
i', j
i', j''
i, j', j
i', j, j''
i, j'
i, j
i', j''
i', j
i, j', j
i', j'', j
(b)
(c)
(d)
(e)

## Slide 43: Graph-Based Verification
Examples of resource conflict graph
(a)
(d)
(b)
(e)
1,1
1,2
2,1
2,2
1,1,2
2,1,2
1,1
1,2
2,1
2,2
2,1,2
1,1,2
1,1
2,2
2,1
2,3
1,3
1,1,3
2,2,3
2,1,2
1,1
2,2
2,1
2,3
1,3
1,1,3
2,2,3
2,1,2
1,1
2,1
1,3
2,2
3,2
3,3
(c)
1,1,3
2,1,2
3,2,3
H'
G'

## Slide 44: Petri-Net-Based Verification
Petri Net Examples
1,1
1,2
1,2,1
2,1,2
1,in
1,out
2,1
2,2
2,in
2,out
(a)
(b)
(d)
(e)
1,1
1,2
1,2,1
1,2,2
1,in
1,out
2,1
2,2
2,in
2,out
1,1
2,1,1
1,in
1,3
1,out
2,1
2,2
2,in
2,out
1,2,3
2,3
1,1
1,2,1
1,in
1,3
1,out
2,1
2,2
2,in
2,out
2,1,3
2,3
1,1
1,in
1,3
1,out
1,2,1
2,1
2,2
2,in
2,out
2,3,2
3,2
3,in
3,out
3,3
3,1,3
(c)
Place
Transition
Token
Arc
Edge in G'

## Slide 45: Summary
A cycle-removal algortihm (not covered today) to
  Minimize
    The passing time of the last vehicle, or
    The average delay of vehicles
  Guarantee collision-freeness
    Provided by the passing order and scheduling after removing cycles
  Guarantee deadlock-freeness
    Graph-based verification
    Petri-Net-based verification
4
1
2
3
1
2
3
4
1,1
1,2
1,3
2,1
3,3
3,4
4,4
4,1
Type-1
Type-2
Type-3

## Slide 46: Outline
Modeling
Controlling Lengths of Traffic Lights
Intelligent Intersection Management
Imperfect Communication
Centralized and Distributed Approaches
Graph-Based Approach
Non-Cooperative Environment

## Slide 47: Game Theory
What is a game?
Prisoner's dilemma
Multiple Rational Decision Makers
Conflicting Interests
Decisions
Players
Actions
Objectives
A Game
 | Prisoner A Stays Silent | Prisoner A Betrays
Prisoner B Stays Silent | Both in Jail for 1 Year | A Goes Free B in Jail for 3 Years
Prisoner B Betrays | A in Jail 3 Years B Goes Free | Both in Jail for 2 Years (Nash Equilibrium)

## Slide 48: Two-Vehicle Scenario (w/o Manager)
Payoff matrix (waiting time) of vehicles A and B
  Case 1 (same priority)
  Case 2 (Vehicle A has a higher priority)
  Where are the Nash Equilibria?
    Are them realistic?  People are not rational (------)
Payoffs of A and B | Vehicle A Enters | Vehicle A Stops
Vehicle B Enters | (-3600, -3600) | (-4, 0)
Vehicle B Stops | (0, -4) | (-3, -3) (Average of -1 and -5)
Payoffs of A and B | Vehicle A Enters | Vehicle A Stops
Vehicle B Enters | (-1800, -7200) | (-4, 0)
Vehicle B Stops | (0, -4) | (-1, -5)

## Slide 49: Three-Vehicle Scenario (with Manager)
Three-vehicle strategic game
  Assume that the time needed to go through an intersection is 7
  Vehicle C does not worsen the overall system performance
    Total delays = 9
  However, Vehicle C can take advantage from it
No Vehicle lies |  |  |  | 
Vehicle | Actual Time | Reported Time | Allocated Time | Delay
A | 5 | 5 | 5 | 0
B | 10 | 10 | 12 | 2
C | 12 | 12 | 19 | 7
System Performance |  |  |  | 9
Vehicle C Lies |  |  |  | 
Vehicle | Actual Time | Reported Time | Allocated Time | Delay
A | 5 | 5 | 5 | 0
B | 10 | 10 | 19 | 9
C | 12 | 6 | 12 | 0
System Performance |  |  |  | 9

## Slide 50
Q&A